## Slide 1
Memory
BRAC University
‹#›
Notes: ‹#›

## Slide 2: What is Memory Unit?
A memory unit is a collection of registers together with associated circuits needed to transfer information in and out of registers.
Binary cell: An elementary unit of computer storage (i.e. memory register) that can have one or the other of two stable states and can thus store one bit of information.
The memory cell is an electronic circuit that stores one bit of binary information and it must be set to store a logic 1 (high voltage level) and reset to store a logic 0 (low voltage level). Its value is maintained/stored until it is changed by the set/reset process.
A memory unit stores binary information in groups of bits called words.
Communication between memory unit and its environment is achieved through 2 controls( read and write) and 2 external registers (memory address register and memory buffer register).
To communicate with a memory word, its address is transferred to memory address register. Internal circuit then opens the path to select that word. A n-bit address register can specify up to 2^n address. (note: # of address=# of word)
Before writing and after reading information are kept in Memory Buffer registers. In each case, the address register specifies location of writing or reading.
‹#›

## Slide 3
‹#›

## Slide 4: READ WRITE Operation Example
‹#›

## Slide 5: Random Access Memory (RAM)
Content of a 1024 x 16-bit memory:
1011010111011101
1010000110000110
0010011101110001
:
:
1110010101010010
0011111010101110
1011000110010101
Memory content
decimal
0
1
2
:
:
1021
1022
1023
0000000000
0000000001
0000000010
:
:
1111111101
1111111110
1111111111
binary
Memory address
‹#›
Notes: ‹#›

## Slide 6: Random Access Memory (RAM)
The data consists of n lines (for n-bit words). Data input lines provide the information to be stored (written) into the memory, while data output lines carry the information out (read) from the memory.
The address consists of k lines which specify which word (among the 2k words available) to be selected for reading or writing.
The control lines Read and Write (usually combined into a single control line Read/Write) specifies the direction of transfer of the data.
Example: A memory unit of 1024 words with 8 bit/word needs, 10 address line (i.e. address register must contain 10 FF) and buffer register must have 8 FF to store words transferred in and out of it.
‹#›
Notes: ‹#›

## Slide 7: Random Access Memory (RAM)
Block diagram of a memory unit:
Memory unit
2k words
n bits per word
k address lines
k
Read/Write
n
n
n data input lines
n data output lines
‹#›
Notes: ‹#›

## Slide 8
‹#›
Notes: ‹#›

## Slide 9: Random Access Memory (RAM)
The Write operation:
  Transfers the address of the desired word to the address lines
  Transfers the data bits (the word) to be stored in memory to the data input lines
  Activates the Write control line (set Read/Write to 0)
The Read operation:
  Transfers the address of the desired word to the address lines
  Activates the Read control line (set Read/Write to 1)
‹#›
Notes: ‹#›

## Slide 10: Random Access Memory (RAM)
The Read/Write operation:
Two types of RAM: Static and dynamic.
  Static RAMs use flip-flops as the memory cells.
  Dynamic RAMs use capacitor charges to represent data. Though simpler in circuitry, they have to be constantly refreshed.
‹#›
Notes: ‹#›

## Slide 11: Memory Size
Memory sizes might be specified in bits or byte(=8bit)
Symbol: Bytes (B) and bits(b)
Example, 2^28 b = 2^28/8 B= 2^28/2^3 B=2^25 B= 2^5*2^20 B = 32 MB
‹#›
 | Prefix | Base 2 | Base 10
K | Kilo | 2^10= 1024 | 10^3=1,000
M | Mega | 2^20 =1,048,576 | 10^6= 1,000,000
G | Giga | 2^30 =1,073,741,824 | 10^9= 1,000,000,000

## Slide 12: 2 formula to remember
Capacity = no. of word x bit/word
No. of word= 2 ^ (address lines)
‹#›
Capacity= 2^(address line) x bit/word

## Slide 13: Test your self
‹#›

## Slide 14
Solution: c
= 2^16 x 16 bits/words
= 1048576 bits
= 1048576/8 bytes
= 131072 bytes
= 131072/1024 KB
= 128 KB
‹#›

## Slide 15: Test yourself
‹#›

## Slide 16: Solution
Answer: C
Formula:
Capacity = no. of word x bit/word
64MB = no. of word x 32bits/word
no. of word = 64MB / 32 bits/word
= (64x1024x1024x8)(/32[ 1 byte = 2^3 bits]
= 16777216 bits = 2^24 bits
no. of address lines = 24
‹#›

## Slide 17: Binary cell
Must be small so that many binary cell (BC) can fit in a small area
Select input enable cell for reading/writing
Read/write determines operation to be preformed on cell. A 1 in read/write input forms a path to the output terminal. A 0 in read/write input, information in the input terminal is transferred into the FF
‹#›

## Slide 18: Random Access Memory (RAM)
A single memory cell of the static RAM has the following logic and block diagrams.
R
S
Q
Input
Select
Output
Read/Write
BC
Output
Input
Select
Read/Write
Logic diagram
Block diagram
‹#›
Notes: ‹#›

## Slide 19: Random Access Memory (RAM)
Logic construction of a 4 x 3 RAM (with decoder and OR gates):
# of word
Bit/word
‹#›
BC
Output
Input
Select
Read/Write
Notes: ‹#›

## Slide 20: Random Access Memory (RAM)
Logic construction of a 2048 x 32 RAM (with decoder and OR gates):
# of word
Bit/word
‹#›
Notes: ‹#›

## Slide 21: Random Access Memory (RAM)
An array of RAM chips: memory chips are combined to form larger memory.
A 1K x 8-bit RAM chip:
Block diagram of a 1K x 8 RAM chip
RAM 1K x 8
DATA (8)
ADRS (10)
CS
RW
Input data
Address
Chip select
Read/write
(8)
Output data
8
8
10
‹#›
Notes: ‹#›