## Slide 1: MSI Circuits

## Slide 2: Useful MSI circuits
Four common and useful MSI circuits are:
  Decoder
  Demultiplexer
  Encoder
  Multiplexer
Block-level outlines of MSI circuits:
decoder
code
entity
encoder
code
entity
mux
data
input
select
demux
data
output
select

## Slide 3: Decoders
Convert binary information from n input lines to (max. of) 2n output lines.
Known as n-to-m-line decoder, or simply n:m or n×m decoder (m ≤ 2n).
May be used to generate 2n (or fewer) minterms of n input variables.

## Slide 4: Decoders
Example: if codes 00, 01, 10, 11 are used to identify four light bulbs, we may use a 2-bit decoder:
2x4
Dec
2-bit code
X
Y
F0 F1 F2 F3
Bulb 0
Bulb 1
Bulb 2
Bulb 3
This is a 2×4 decoder which selects an output line based on the 2-bit code supplied.
Truth table:

## Slide 5: Decoders
From truth table, circuit for 2×4 decoder is:
Note: Each output is a 2-variable minterm (X'Y', X'Y, XY' or XY)
F0 = X'Y'
F1 = X'Y
F2 = XY'
F3 = XY
X
Y

## Slide 6: Decoders
Design a 3×8 decoder by yourself.

## Slide 7: Solution

## Slide 8: Decoders
In general, for an n-bit code, a decoder could select up to 2n lines:
:
:
n-bit
code
n to 2n
decoder
up to 2n
output lines
As n input generates 2^n output, which reminds us of canonical SOP, thus a decoder can be used to generate any function

## Slide 9: Application of Decoder
Example 1: Full adder circuit with decoder (3 x 8 decoder)

## Slide 10: Demultiplexer
Given an input line and a set of selection lines, the demultiplexer will direct data from input to a selected output line.
An example of a 1-to-4 demultiplexer:
demux
Data D
Outputs
select
S1 S0
Y0 = D.S1'.S0'
Y1 = D.S1'.S0
Y2 = D.S1.S0'
Y3 = D.S1.S0

## Slide 12: Demultiplexer
The demultiplexer is actually identical to a decoder with enable. A decoder with an enable input can function as a demultiplexer (or demux) Decoder + enable= demultiplexer
The selection of a specific output line is controlled by the bit values of ‘n’-selection lines.
2x4 Decoder
D
S1
S0
Y0 = D.S1'.S0'
Y1 = D.S1'.S0
Y2 = D.S1.S0'
Y3 = D.S1.S0
E
demux
data
output
select

## Slide 13: 4-line-to-16 line Decoder constructed with two 3-line-to-8 line decoders with enables

## Slide 14: 4-line-to-16 line Decoder constructed with two 3-line-to-8 line decoders with enables
When w=0, the top decoder is enabled and the other is disabled. The bottom decoder outputs are all 0’s , and the top eight outputs generate min-terms 0000 to 0111.
When w=1, the enable conditions are reversed. The bottom decoder outputs generate min-terms 1000 to 1111, while the outputs of the top decoder are all 0’s.

## Slide 15
F(a,b,c,d)=∑(0,1,3,5,12,13)
Implement the above boolean function using
3:8 Decoder(s).
2:4 Decoder(s).

## Slide 16
F(a,b,c,d)=∑(0,1,3,5,12,13)
Implement the above boolean function using
3:8 Decoder(s).
2:4 Decoder(s).
You have to connect D0,D1,D3,D5,D12 & D13 with OR Gate

## Slide 17: Multiplexer
A multiplexer is a device which has
(i) a number of input lines
(ii) a number of selection lines
(iii) one output line
A Multiplexer steers one of 2n inputs to a single output line, using n selection lines. Also known as a data selector.
2n:1
Multiplexer
output
inputs
:
select
...

## Slide 18: Multiplexer
Truth table for a 4-to-1 multiplexer:
mux
Y
Inputs
select
S1 S0
I0
I1
I2
I3
4:1
MUX
Y
Inputs
select
S1 S0
I0
I1
I2
I3
0
1
2
3
Output

## Slide 20: Multiplexer
Output of multiplexer is
“sum of the (product of data lines and selection lines)”
Often known as Data selector as it selects one of the many inputs and steers the binary information to the output line.
Example: the output of a 4-to-1 multiplexer is:
Y = I0.(S1’.S0') + I1.(S1’.S0) + I2.(S1.S0') + I3.(S1.S0)

## Slide 21: Try it yourself
Draw the internal circuit diagram (logic diagram) of a 4-to-1 multiplexer.
Solution
Y = I0.(S1’.S0') + I1.(S1’.S0) + I2.(S1.S0') + I3.(S1.S0)

## Slide 22: Larger Multiplexers
Larger multiplexers can be constructed from smaller ones.
An 8-to-1 multiplexer can be constructed from smaller multiplexers like this (from two 4x1 and one 2x1):

## Slide 23: Larger Multiplexers
Larger multiplexers can be constructed from smaller ones.
An 8-to-1 multiplexer can be constructed from smaller multiplexers like this (from two 4x1 and one 2x1):
4:1 MUX
I0
I1
I2
I3
S1 S0
4:1 MUX
I4
I5
I6
I7
S1 S0
2:1 MUX
S2
Y
I0
I4
I0
When
S2S1S0 = 000

## Slide 24: Larger Multiplexers
Another implementation of an 8-to-1 multiplexer using smaller multiplexers (four 2x1 and one 4x1):

## Slide 25: Larger Multiplexers
Another implementation of an 8-to-1 multiplexer using smaller multiplexers (four 2x1 and one 4x1):
Y
I0
When
S2S1S0 = 000
4:1 MUX
S2 S1
I0
I1
2:1 MUX
S0
I2
I3
2:1 MUX
S0
I4
I5
2:1 MUX
S0
I6
I7
2:1 MUX
S0
I0
I4
I2
I6
Q: Can we use only 2:1 multiplexers?

## Slide 26: Larger Multiplexers
Q: Can we use only 2:1 multiplexers?

## Slide 27: Try it yourself: Larger Multiplexers
A 16-to-1 multiplexer can be constructed from only 4-to-1 multiplexers:

## Slide 28: Encoder
Encoder is a digital function that produces a reverse operation of a decoder!
It has 2n input lines and n output lines

## Slide 29: Example: Octal-binary encoder

## Slide 30: Example: Octal-binary encoder
There are 8 input variables so there will 28 input combination, amongst which in Octal-binary encoder only 8 are useful

## Slide 31: Example: Priority Encoder
Design a priority encoder, which will allow more than one input to exist and encodes only the highest priority input line. For example, 8x3 encoder in a if user give D2 and D7 together, it will allow data of D7 to pass.

## Slide 32: Priority Encoder
  Accepts multiple values and encodes them
    Works when more than one input is active
  Consists of:
    Inputs (2n)
    Outputs
      when more than one output is active, sets output to correspond to highest input
      V (indicates whether any of the inputs are active). This helps to show the output when all inputs are 0s
    Selectors / Enable
Notes: 32

## Slide 33
D3 | D2 | D1 | D0 | A1 | A0 | V
0 | 0 | 0 | 0 | x | X | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Note: Amongst all 3 input, D2 is highest so output reflects the binary value of 2
Note: V is not really an output, just shows whether there is an active input or not.

## Slide 34: Priority Encoder

## Slide 35: Priority Encoder

## Slide 36: Boolean Function implementation using MSI

## Slide 37: Try it yourself
Using 4:1 MUX design
AND gate
OR gate
NOT gate
GND
+5v
AND
GND
+5v
GND
+5v
OR
NOT
X
X

## Slide 38: Try it yourself
a)Built the following function using 8x1 Mux.
F=∑(0,4,5) b)Design same thing with 3x8 decoder
c) Try designing it with single 4x1 Mux

## Slide 39: Solution
F=∑(0,4,5)
5V
b)
a)

## Slide 40: Rules: for using smaller mux to build larger equation
1 A 0 0
B C
1 A
0
0
Answer: Part ( c )

## Slide 41: Built the following function using 4x1 Mux

## Slide 42: Try it yourself
Implement the below function using a 8x1 Mux.
Implement the below function using a 4x16 decoder and OR gates

## Slide 43: Solution
a)

## Slide 44: Home-task: Try it yourself
Using 2:1 MUX design
AND gate
OR gate
NOT gate
Solution: Try YOUTUBE

## Slide 45: Note:
Both mux and decoder can be used to design combinational circuit.
Decoder are mostly used to decoding binary information and mux are mostly used to select path between multiple sources and a single destination.

## Slide 46
4 variables with 4x1 Mux
https://www.youtube.com/watch?v=c8lhlAX2JMk

## Slide 47
F(a,b,c,d)=∑(0,1,4,5,9,14,15)
Implement the above boolean function using 4:1 MUX(s) and 2:1 MUX(s).

## Slide 48: Combining MSI to build Combinational Design Circuit

## Slide 49: Exercise time!
Design a BCD to Excess 3 code converter using ‘4x16’ decoder and ‘16x4’ encoder

## Slide 50: Solution
16:4 encoder

## Slide 51: Try it yourself
Design a full adder using ‘3x8’ decoder and ‘4x2’ encoder

## Slide 52: Solution: